## Slide 1
power flow models
(algebraic equations)
dynamic models
(ODEs)
market
dynamics
Notes: This is how frequency control and market dispatch sit next to each other across the timescale and there is an obvious hierarchical structure for the two operations.
However, what if we want to have a sub-min market for flexible resources? It seems the hierarchy won’t hold and we would have frequency control and market dispatch overlapping each other.
Then why not just combine them because essentially they are doing the same thing – which is controlling supply or demand for power rebalance, just at different timescales originally.
This comes to what we call market dynamics.
xxx
The goal of realizing the underlying economic efficiency through market becomes even more challenging in real life in light of the physical power grid. In industry, to prioritize reliability, the norm has been to adopt an operational hierarchy across timescales with market economic dispatch spanning five-minute intervals or longer; and frequency control required to function within one minute or so. There is a buffer period under five minutes for reliability where efficiency is lost. Such a paradigm is a compromise at its best because a higher-frequency market always better handles system variability and approaches finer-granularity efficiency, but in return it might destabilize the grid. This tradeoff motivates my work on coupled electricity grid and market that aims to explore the fundamental limit of how fast a market can be operated without jeopardizing grid reliability.